## Slide 1: ENMT 4730 SLAM Implementation
Eric Borcherding

## Slide 2
Artificial Intelligence (AI)

## Slide 3
Problem Statement
Objectives
Required Hardware
Design
Sensors
Navigation

## Slide 4: Problem Statement
Apply localization, mapping, and path planning techniques discussed in 4730 Advance Ground Robotics class.
  Utilize a wirelessly controlled ground robot, vision system and python programming language.

## Slide 5: Objectives
Localize ground robot in environment utilizing computer vision
Track ground robot as it moves around an ‘obstacle’ course.
Generate a map of navigable terrain while the robot moves
Path plan to generate return path to starting position

## Slide 6: Equipment List
Hardware:
  Robot: Sphero
  Vision System: 720P webcam
  Communication: Bluetooth Dongle
Software:
  Language: Python
  Vision Toolkit: OpenCV
  Analysis Toolkit: Scikit Learn

## Slide 7
Concept
Low cost ground robot
High value overhead processing planning drone

## Slide 8
Concept

## Slide 9: Robot Design
Sphero:
  Holonomic robot
    Manipulates internal mass to steer, accelerate and decelerate
    Independent motors used to move mass in sphere
      Motors drive same direction: Mass is raised allowing sphero to rotate forwards

## Slide 10: Robot Design
Sphero:
  Holonomic robot, capable of turning in place
    Manipulates internal mass to steer, accelerate and decellerate
    Independent motors used to move mass in sphere
      Motors drive same direction: Mass is raised allowing Sphero to rotate forwards
        Sphero stops by returning mass to position of lowest potential energy
      Motors counter rotate: Mass rotates inside shell, causing Sphero to change direction of rotation

## Slide 11: Robot Design

## Slide 12: Localization
Two Stage Localization:
  HSV (Hue, Saturation, Value) Filter
    HSV separates image intensity from color information
    Commonly used in computer vision because of robustness to changing light conditions
  Hough Circle Transform
    Detects outer diameter of robot
      Returns position of robot within reference frame
        This position is used to initialize tracking algorithm

## Slide 13: Localization - HSV Filter

## Slide 14: Localization - Hough Transform

## Slide 15: Tracking
BOOSTING Tracker
  Identify area of interest (utilize Localization data)
  Tracker generates reference image/features.
  Scans video frames to identify reference image, updates location of object being tracked.
    Utilizes data from previous frames to predict how wide an area it must search to identify object of interest
    Determines based on probability where the object is in new field of interest

## Slide 16: Tracking

## Slide 17: Mapping
Enviroment:
  Developed a course for the Sphero to navigate through
  Intent was to map course as it progressed

## Slide 18: Mapping
Reduced Field of View:
  Reduced viewable area to simulate drone following overhead
  Implented HSV filter to determine navigable vs. non-navigable terrain
Full World View
Drone View
Navigable Map

## Slide 19: Mapping

## Slide 20: Mapping

## Slide 21: Path Finding
A* Path Planning
  Heuristic based approach

## Slide 22: Conclusion
Implemented and demonstrated several techniques used in Ground Robotics. Including:
  Localization
  Mapping
  Path Planning