## Slide 1: ENMT 4730 SLAM Implementation
Eric Borcherding

## Slide 2: Overview
Project Focus
  Objectives
Equipment List
Concept
Robot Design
SLAM Implementation
  Localization
  Tracking
  Mapping
  Path Planning

## Slide 3: Project Focus
Apply localization, mapping, and path planning techniques discussed in 4730 Advance Ground Robotics class.
  Utilize a wirelessly controlled ground robot, vision system and python programming language.

## Slide 4: Objectives
Localize ground robot in an environment utilizing computer vision
Track ground robot as it moves around an ‘obstacle’ course.
Generate a map of navigable terrain while the robot moves
Path plan to a location within the generated navigable terrain map

## Slide 5: Equipment List
Hardware:
  Robot: Sphero
  Vision System: 720P-RGB webcam
  Communication: Bluetooth Dongle
Software:
  Language: Python
  Vision Toolkit: OpenCV
  Analysis Toolkit: Scikit Learn

## Slide 6
Concept
Low cost ground robot
High value overhead processing planning drone

## Slide 7
Concept

## Slide 8: Robot Design
Sphero:
  Holonomic robot
    Manipulates internal mass to steer, accelerate and decelerate
    Two independent motors used to move mass in sphere
      Motors drive same direction: Mass is raised allowing Sphero to roll forwards

## Slide 9: Robot Design
Sphero:
  Holonomic robot
    Manipulates internal mass to steer, accelerate and decelerate
    Two independent motors used to move mass in sphere
      Motors drive same direction: Mass is raised allowing Sphero to roll forwards
        Sphero stops by returning mass to position of lowest potential energy
      Motors counter rotate: Mass rotates inside shell, causing Sphero to change direction of rotation

## Slide 10: Robot Design – Sphero Control

## Slide 11: Localization
Multi-Step Localization:
  HSV (Hue, Saturation, Value) Filter
    HSV separates image intensity from color information
    Commonly used in computer vision because of robustness to changing light conditions
  Hough Circle Transform
    Detects outer diameter of robot
      Returns position of robot within reference frame
        This position is used to initialize tracking algorithm
Pictures: https://en.wikipedia.org/wiki/HSL_and_HSV
RGB Color Cube
HSV Color Wheel

## Slide 12: Localization - HSV Filter

## Slide 13: Localization - Hough Transform

## Slide 14: Tracking
Tracking Goals:
  Implement algorithm that tracks position of Sphero as it travels around the course. Needs to return robot position
BOOSTING Tracker
  Identify area of interest (utilize Localization data)
    Tracker generates reference image/features.
  Scans video frames to identify reference image, updates location of object being tracked.
    Utilizes data from previous frames to predict how wide an area it must search to identify object of interest
    Determines based on probability where the object is in new field of interest
Chart: https://www.researchgate.net/publication/309367280_Comparison_of_tracking_algorithms_implemented_in_OpenCV

## Slide 15: Tracking

## Slide 16: Mapping
Enviroment:
  Developed a course for the Sphero to navigate through
  Mapping Goals: Map course as Sphero travels though it. Output navigable terrain so future missions can utilize path planning.

## Slide 17: Mapping
Drone View:
  Reduced viewable area to simulate drone following overhead
  Implented HSV filter to determine navigable vs. non-navigable terrain.
  Utilized edge detection to identify walls
Full World View
Drone View
Navigable Map

## Slide 18: Mapping

## Slide 19: Mapping - Results

## Slide 20: Path Planning
A* Path Planning
  Goal based path planning algorithm. Determines direction of lowest cost (‘distance’). Generates path through navigable terrain
Navigable Map, with end goal (star)
A* Example
Picture: http://theory.stanford.edu/~amitp/GameProgramming/AStarComparison.html

## Slide 21: Path Planning
A* Path Planning
  Goal based path planning algorithm. Determines direction of lowest cost (‘distance’). Generates path through navigable terrain
Navigable Map, with end goal (star)
A* results (blue line)

## Slide 22: Conclusion
Implemented and demonstrated several techniques used in Ground Robotics, including:
  Localization
    HSV Filter
    Hough Circle Transform
    Tracking Algorithm implementation
  Mapping
    HSV Filter
    Mapped Navigable/Non-Navigable terrain
    Utilized Canny Edge detection to identify walls
  Path Planning
    Developed A* path planning algorithm

## Slide 23: Questions